## Slide 1
Constructive Computer Architecture
Sequential Circuits:
Circuits with state
Arvind
Computer Science & Artificial Intelligence Lab.
Massachusetts Institute of Technology
Notes: (Andy) Changed course website to correct website

## Slide 2: Combinational circuits
OpSelect
- Add, Sub, ...
- And, Or, Xor, Not, ...
- GT, LT, EQ, Zero, ...
Result
Comp?
A
B
ALU
Sel
O
A0
A1
An-1
Mux
.
.
.
lg(n)
Sel
O0
O1
On-1
A
Demux
.
.
.
lg(n)
A
Decoder
.
.
.
O0
O1
On-1
lg(n)
Such circuits have no cycles (feedback) or state elements

## Slide 3: Edge-Triggered Flip flop: the basic storage element
ff
Q
D
C
C
D
Q
Metastability
Data is sampled at the rising edge of the clock and must be stable at that time
Unstable data
Notes: Metastability?

## Slide 4: Flip-flops with Write Enables: The building block of Sequential Circuits
ff
Q
D
C
EN
C
D
Q
EN
ff
Q
D
C
EN
0
1
Data is captured only if EN is on
EN | D | Qt | Qt+1
0 | X | 0 | 0
0 | X | 1 | 1
1 | 0 | X | 0
1 | 1 | X | 1
hold
copy
input
No need to show clock explicitly
Notes: Why dangerous?
Glitches

## Slide 5: Registers
Register: A group of flip-flops with a common
clock and enable
Register file: A group of registers with a common
clock, input and output port(s)
ff
D
ff
D
ff
D
ff
D
ff
D
ff
D
ff
D
ff
Q
Q
Q
Q
Q
Q
Q
Q
D
C
En

## Slide 6: An example Modulo-4 counter
Prev State | NextState | 
q1q0 | inc = 0 | inc = 1
00 | 00 | 01
01 | 01 | 10
10 | 10 | 11
11 | 11 | 00
q0t+1 = ~inc∙q0t + inc∙~q0t
= inc  q0t
q1t+1 = ~inc∙q1t + inc∙~q1t∙q0t + inc∙q1t∙~q0t
= (inc == 1) ? q0t  q1t : q1t
00
01
10
11
inc=1
inc=1
inc=1
inc=1
inc=0
inc=0
inc=0
inc=0
Finite State Machine (FSM) representation
Notes: State diagram – replace Cnt by inc

## Slide 7: Finite State Machines (FSM) and Sequential Ckts
FSMs are a mathematical object like the Boolean Algebra
  A computer (in fact any digital hardware) is an FSM
Synchronous Sequential Circuits is a method to implement FSMs in hardware
  Large circuits need to be described as a collection of cooperating FSMs
  State diagrams and next-state tables are not suitable for such descriptions
output
input
Combinational
logic
state
Next state
clock

## Slide 8: Modulo-4 counter in BSV
interface Counter;
method Action inc;
method Bit#(2) read;
endinterface
module moduloCounter(Counter);
Reg#(Bit#(2)) cnt <- mkReg(0);
method Action inc;
cnt <={cnt[1]^cnt[0],~cnt[0]};
endmethod
method Bit#(2) read;
return cnt;
endmethod
endmodule
Modulo-4
counter
inc
read
2
An action to specify how the value of the cnt is to be set
State specification
Initial value

## Slide 9: Modules
A module in BSV is like a class definition in Java or C++
  It has internal state
  The internal state can only be read and manipulated by the (interface) methods
  An action specifies which state elements are to be modified
  Actions are atomic -- either all the specified state elements are modified or none of them are modified (no partially modified state is visible)
interface Counter;
method Action inc;
method Bit#(2) read;
endinterface

## Slide 10: Inside the Modulo-4 counter
inc
cnt0
cnt1
1
0
module moduloCounter(Counter);
Reg#(Bit#(2)) cnt <- mkReg(0);
method Action inc;
cnt <={cnt[1]^cnt[0],~cnt[0]};
endmethod
method Bit#(2) read;
return cnt;
endmethod
endmodule
read
2

## Slide 11: Examples

## Slide 12: A hardware module for computing GCD
Euclid’s algorithm for computing the Greatest Common Divisor (GCD):
15 6
9 6 subtract
3 6 subtract
6 3 swap
3 3 subtract
0 3 subtract
answer
gcd (a,b) = if a==0 then b \\ stop
else if a>=b then gcd(a-b,b) \\ subtract
else gcd (b,a) \\ swap

## Slide 13: GCD module
start
GCD
busy
getResult
ready
en
en
interface GCD;
method Action start (Bit#(32) a, Bit#(32) b);
method ActionValue#(Bit#(32)) getResult;
method Bool busy;
method Bool ready;
endinterface
GCD can be started if the module is not busy;
Results can be read when ready
data
result

## Slide 14: GCD in BSV
module mkGCD (GCD);
Reg#(Bit#(32)) x <- mkReg(0);
Reg#(Bit#(32)) y <- mkReg(0);
Reg#(Bool) busy_flag <- mkReg(False);
rule gcd;
if (x >= y) begin x <= x – y; end //subtract
else if (x != 0) begin x <= y; y <= x; end //swap
endrule
method Action start(Bit#(32) a, Bit#(32) b);
x <= a; y <= b; busy_flag <= True;
endmethod
method ActionValue#(Bit#(32)) getResult;
busy_flag <= False; return y;
endmethod
method busy = busy_flag;
method ready = x==0;
endmodule
Assume b /= 0
start should be called only if the module is not busy;
getResult should be called only when ready is true.

## Slide 15: Rule
rule gcd;
if (x >= y) begin x <= x – y; end //subtract
else if (x != 0) begin x <= y; y <= x; end //swap
endrule
parallel composition of actions
A rule is a collection of actions, which invoke methods
All actions in a rule execute in parallel
A rule can execute any time and when it executes all of its actions must execute
atomicity
A module may contain rules

## Slide 16: Parallel Composition of Actions & Double-Writes
Parallel composition, and consequently a rule containing it, is illegal if a double-write possibility exists
The BSV compiler rejects a program if it there is a possibility of a double write
rule one;
y <= 3; x <= 5; x <= 7; endrule
Double write
Possibility of a double write
No double write
rule two;
y <= 3; if (b) x <= 7; else x <= 5; endrule
rule three;
y <= 3; x <= 5; if (b) x <= 7; endrule

## Slide 17: Defining FIFOs and it’s uses

## Slide 18: FIFO Module Interface
interface Fifo#(numeric type size, type t);
method Bool notFull;
method Bool notEmpty;
method Action enq(t x);
method Action deq;
method t first;
endinterface
x
en
en
enq
deq
Fifo
module
!full
!emty
first
notFull
notEmpty
first
- enq should be called only if notFull returns True;
- deq and first should be called only if notEmpty returns True

## Slide 19: An Implementation: One-Element FIFO
module mkFifo (Fifo#(1, t));
Reg#(t) d <- mkRegU;
Reg#(Bool) v <- mkReg(False);
method Bool notFull;
return !v;
endmethod
method Bool notEmpty;
return v;
endmethod
method Action enq(t x);
v <= True; d <= x;
endmethod
method Action deq;
v <= False;
endmethod
method t first;
return d;
endmethod
endmodule
x
en
en
enq
deq
Fifo
module
!full
!emty
first
notFull
notEmpty
first

## Slide 20: Streaming a function
inQ
f
outQ
rule stream;
if(inQ.notEmpty && outQ.notFull)
begin outQ.enq(f(inQ.first)); inQ.deq; end endrule
Boolean & (“AND”) operation

## Slide 21: Streaming a module
outQ
inQ
rule invokeGCD;
if(inQ.notEmpty && !gcd.busy)
begin gcd.start(inQ.first); inQ.deq; end endrule
start
GCD
busy
result
ready
invoke
GCD
get
result
rule getResult;
if(outQ.notFull && gcd.ready)
begin x <- gcd.result; outQ.enq(x); end
endrule
Action value method

## Slide 22: Switch red messages go into redQ, green into greenQ
rule switch;
if (inQ.first.color == Red) begin
redQ.enq(inQ.first.value); inQ.deq;
end
else begin
greenQ.enq(inQ.first.value); inQ.deq;
end;
endrule
The code is not correct because it does not include tests for empty inQ or full redQ or full greenQ conditions!
inQ
redQ
greenQ
switch
red messages go into redQ, green into greenQ
Notes: Effect of inQ.deq is not visible to inQ.first

## Slide 23: Switch with empty/full tests on queues - 1
inQ
redQ
greenQ
switch
rule switch;
if (inQ.first.color == Red) begin
redQ.enq(inQ.first.value); inQ.deq;
end
else begin
greenQ.enq(inQ.first.value); inQ.deq;
end
endrule
first and deq operations can be performed only if inQ is not empty

## Slide 24: Switch with empty/full tests on queues -2
inQ
redQ
greenQ
switch
rule switch;
if (inQ.notEmpty)
if (inQ.first.color == Red) begin
redQ.enq(inQ.first.value); inQ.deq;
end
else begin
greenQ.enq(inQ.first.value); inQ.deq;
end
endrule
When can an enq operation be performed on redQ?

## Slide 25: Switch with empty/full tests on queues
inQ
redQ
greenQ
switch
rule switch;
if (inQ.notEmpty)
if (inQ.first.color == Red) begin1
if (redQ.notFull) begin2
redQ.enq(inQ.first.value); inQ.deq;
end2
end1
else begin3
if (greenQ.notFull) begin4
greenQ.enq(inQ.first.value); inQ.deq;
end4
end3
endrule

## Slide 26: An optimization
inQ
redQ
greenQ
switch
rule switch;
if (inQ.notEmpty)
if (inQ.first.color == Red) begin1
if (redQ.notFull) begin2
redQ.enq(inQ.first.value); inQ.deq;
end2
end1
else begin3
if (greenQ.notFull) begin4
greenQ.enq(inQ.first.value); inQ.deq;
end4
end4
endrule
inQ.deq;
endrule
Can we move the deq here?
inQ value may get lost if redQ (or greenQ) is full
Atomicity violation!
A wrong optimization

## Slide 27: Observations
These sample programs are not very complex and yet it would have been tedious to express these programs in a state table or as a circuit directly
The meaning of double-write errors is not standardized across Verilog tools
Interface methods are not available in Verilog/VHDL