## Slide 1
Constructive Computer Architecture:
Scheduling Constraints on Interface methods
Arvind
Computer Science & Artificial Intelligence Lab.
Massachusetts Institute of Technology

## Slide 2: “Happens before” (<) relation
“happens before” relation between the methods of a module governs how the methods behave when called by a rule, action, method or exp
  f < g : f happens before g
  (g cannot affect f within an action)
  f > g : g happens before f
  C : f and g conflict and cannot be called together
  CF : f and g are conflict free and do not affect each
  other
This relation is defined as a conflict matrix (CM) for the methods of primitive modules like registers and derived for the methods of all other modules

## Slide 3: Conflict Matrix for an Interface
Conflict Matrix (CM) defines which methods of a module can be called concurrently
CM for a register:
  Two reads can be performed concurrently
  Two concurrent writes conflict and are not permitted
  A read and a write can be performed concurrently and it behaves as if the read happened before the write
CM of a register is used systematically to derive the CM for the interface of a module and the CM for rules
 | reg.r | reg.w
reg.r | CF | <
reg.w | > | C

## Slide 4: Conflict ordering
There is a natural ordering between the values of CM entries
This ordering permits us to take intersections of conflict information, e.g.,
  {>}{<,>} = {>}
  {>}{<} = {}
CF = {<,>}
{<} {>}
C = {}

## Slide 5: Deriving the Conflict Matrix (CM) of a module interface
Let g1 and g2 be the two methods defined by a module, such that
  mcalls(g1)={g11,g12...g1n}
  mcalls(g2)={g21,g22...g2m}
conflict(x,y) = if x and y are methods of the same module then CM[x,y] else CF
Derivation
  CM[g1,g2] = conflict(g11,g21)  conflict(g11,g22) ...
   conflict(g12,g21)  conflict(g12,g22) ...
  …
   conflict(g1n,g21)  conflict(g1n,g22) ...
Conflict relation is not transitive
  m1.g1 < m2.g2, m2.g2 < m3.g3 does not imply m1.g1 < m3.g3
Compiler can derive the CM for a module by starting with the innermost modules in the module instantiation tree
Methods called by g1

## Slide 6: Two-Element FIFO Deriving the CM
method Action enq(t x) if (!vb);
if (va) begin db <= x; vb <= True; end
else begin da <= x; va <= True; end
endmethod
method Action deq if (va);
if (vb) begin da <= db; vb <= False; end
else begin va <= False; end
endmethod
db da
vb va
We can derive a conservative CM by ignoring the conditionals
mcalls(enq) = {vb.r, va.r, db.w, vb.w, da.w, va.w}
mcalls(deq) = {va.r, vb.r, da.w, db.r, vb.w, va.w}
  CM[enq,deq] =
  CM[vb.r,va.r]CM[vb.r, vb.r]CM[vb.r,da.w]CM[vb.r,db.r]CM[vb.r,vb.w]CM[vb.r,va.w]
  CM[va.r,va.r]CM[va.r, vb.r]CM[va.r,da.w]CM[va.r,db.r]CM[va.r,vb.w]CM[va.r,va.w]
  CM[db.w,va.r]CM[db.w,vb.r]CM[db.w,da.w]CM[db.w,db.r]CM[db.w,vb.w]CM[db.w,va.w]
  CM[vb.w,va.r]CM[vb.w,vb.r]CM[vb.w,da.w]CM[vb.w,db.r]CM[vb.w,vb.w]CM[vb.w,va.w]
  CM[da.w,va.r]CM[da.w,vb.r]CM[da.w,da.w]CM[da.w,db.r]CM[da.w,vb.w]CM[da.w,va.w]
  CM[va.w,va.r]CM[va.w,vb.r]CM[va.w,da.w]CM[va.w,db.r]CM[va.w,vb.w]CM[va.w,va.w]
  = CF  {<}  CF  {<}  {>}  {>}  C  C  {>}  C
  = C

## Slide 7: Two-Element FIFO another implementation
module mkCFFifo (Fifo#(2, t));
Reg#(t) da <- mkRegU();
Reg#(Bool) va <- mkReg(False);
Reg#(t) db <- mkRegU();
Reg#(Bool) vb <- mkReg(False)
rule canonicalize if (vb && !va);
da <= db;
va <= True; vb <= False; endrule
method Action enq(t x) if (!vb);
begin db <= x; vb <= True; end
endmethod
method Action deq if (va);
va <= False;
endmethod
method t first if (va); return da;
endmethod
endmodule
Can both enq and deq execute concurrently?
yes
db da
vb va
But neither enq or deq execute again until the canonicalize rule fires!
…and canonicalize cannot execute concurrently with enq and deq!
 Dead-cycle

## Slide 8: Limitations of registers
Can’t express a FIFO with concurrent enq and deq with no dead cycles!
It is because in a language with only the register primitive no communication can take place in the same atomic action (i.e. clock cycle) between two methods or between two rules or between a rule and a method
EHRs to rescue …

## Slide 9: EHR: Ephemeral History Register
A new primitive element to design modules with concurrent methods

## Slide 10: Ephemeral History Register (EHR) Dan Rosenband [MEMOCODE’04]
D
Q
0
1
0
1
w[0].data
w[0].en
r[0]
normal
bypass
r[1]
w[1].data
w[1].en
r[0] < w[0]
w[0] < w[1] < ….
r[1] < w[1]
r[1] returns:
– the current state if w[0] is not enabled
– the value being written (w[0].data) if w[0] is enabled
w[i+1] takes precedence over w[i]

## Slide 11: Conflict Matrix of Primitive modules: Registers and EHRs
 | EHR.r0 | EHR.w0 | EHR.r1 | EHR.w1
EHR.r0 |  |  |  | 
EHR.w0 |  |  |  | 
EHR.r1 |  |  |  | 
EHR.w1 |  |  |  | 
 | reg.r | reg.w
reg.r | CF | <
reg.w | > | C
Register
EHR
CF
>
CF
>
<
C
>
>
CF
<
CF
>
<
<
<
C

## Slide 12: Designing FIFOs using EHRs
Conflict-Free FIFO: Both enq and deq are permitted concurrently as long as the FIFO is not-full and not-empty
  The effect of enq is not visible to deq, and vise versa
Pipeline FIFO: An enq into a full FIFO is permitted provided a deq from the FIFO is done simultaneously
Bypass FIFO: A deq from an empty FIFO is permitted provided an enq into the FIFO is done simultaneously
We will derive such FIFOs starting with one and two element FIFO designs

## Slide 13: Making One-Element FIFO into a Pipelined FIFO
module mkFifo (Fifo#(1, t));
Reg#(t) d <- mkRegU;
Reg#(Bool) v <- mkReg(False);
method Action enq(t x) if (!v);
v <= True; d <= x;
endmethod
method Action deq if (v);
v <= False;
endmethod
method t first if (v);
return d;
endmethod
endmodule
Pipelined FIFO behavior
deq < enq
first < deq
first < enq
Ehr#(2, Bool) v <- mkEhr(False);
v[0]
(v[0]);
(v[0]);
v[1]
(!v[1]);
No double write error

## Slide 14: One-Element Pipelined FIFO
module mkPipelineFifo(Fifo#(1, t));
Reg#(t) d <- mkRegU;
Ehr#(2, Bool) v <- mkEhr(False);
method Action enq(t x) if (!v[1]);
d <= x;
v[1] <= True;
endmethod
method Action deq if (v[0]);
v[0] <= False;
endmethod
method t first if (v[0]);
return d;
endmethod
endmodule
deq < enq
first < deq
first < enq
In any given cycle:
If the FIFO is not empty then simultaneous enq and deq are permitted;
Otherwise, only enq is permitted

## Slide 15: Making One-Element FIFO into a Bypass FIFO
module mkFifo (Fifo#(1, t));
Reg#(t) d <- mkRegU;
Reg#(Bool) v <- mkReg(False);
method Action enq(t x) if (!v);
v <= True; d <= x;
endmethod
method Action deq if (v);
v <= False;
endmethod
method t first if (v);
return d;
endmethod
endmodule
v[1]
(v[1]);
(v[1]);
v[0]
(!v[0]);
No double write error
Bypass FIFO behavior
enq < deq
first < deq
enq < first
d[1];
Ehr#(2, t) d <- mkEhr(?);
Ehr#(2, Bool) v <- mkEhr(False);
d[0] <= x;

## Slide 16: One-Element Bypass FIFO
module mkBypassFifo(Fifo#(1, t));
Ehr#(2, t) d <- mkEhr(?);
Ehr#(2, Bool) v <- mkEhr(False);
method Action enq(t x) if (!v[0]);
d[0] <= x;
v[0] <= True;
endmethod
method Action deq if (v[1]);
v[1] <= False;
endmethod
method t first if (v[1]);
return d[1];
endmethod
endmodule
Desired behavior
enq < deq
first < deq
enq < first
In any given cycle:
If the FIFO is not full then simultaneous enq and deq are permitted;
Otherwise, only deq is permitted

## Slide 17: Making a Two-Element Conflict-Free FIFO
module mkCFFifo (Fifo#(2, t));
Reg#(t) da <- mkRegU();
Reg#(Bool) va <- mkReg(False);
Reg#(t) db <- mkRegU();
Reg#(Bool) vb <- mkReg(False)
rule canocalize (vb && !va);
da <= db; va <= True;
vb <= False; endrule
method Action enq(t x) if (!vb);
db <= x; vb <= True;
endmethod
method Action deq if (va);
va <= False;
endmethod
method t first if (va);
return da; endmethod
endmodule
db da
vb va
Desired behavior
enq CF deq
first < deq
first CF enq
Turn all registers into EHRs
Let enq and deq read and write 0th port
Let canocalize read and write the 1st port

## Slide 18: Two-Element Conflict-free FIFO
module mkCFFifo(Fifo#(2, t))
Ehr#(2, t) da <- mkEhr(?);
Ehr#(2, Bool) va <- mkEhr(False);
Ehr#(2, t) db <- mkEhr(?);
Ehr#(2, Bool) vb <- mkEhr(False);
rule canonicalize (vb[1] && !va[1]);
da[1] <= db[1]; va[1] <= True;
vb[1] <= False; endrule
method Action enq(t x) if (!vb[0]);
db[0] <= x; vb[0] <= True;
endmethod
method Action deq if (va[0]);
va[0] <= False;
endmethod
method t first if (va[0]);
return da[0]; endmethod
endmodule
Desired behavior
enq CF deq
first < deq
first CF enq
In any given cycle:
Simultaneous enq and deq are permitted only if the FIFO is not full and not empty
db da
vb va

## Slide 19: CM for Pipelined FIFO
method Action enq(t x) if (!v[1]);
d <= x; v[1] <= True; endmethod
method Action deq if (v[0]);
v[0] <= False; endmethod
method t first if (v[0]);
return d; endmethod
mcalls(enq)={v.r1, d.w, v.w1}
mcalls(deq)={v.r0, v.w0}
mcalls(first)={v.r0, d.r}
= {>}  {>} = {>}
conflict[v.r1,v.r0]  conflict[v.r1,v.w0]  conflict[d.w,v.r0]  conflict[d.w,v.w0]  conflict[v.w1,v.r0]  conflict[v.w1,v.w0]
This is what we expected!
 | Enq | Deq | First
Enq | C | > | >
Deq | < | C | >
First | < | < | CF
CM[enq,deq]=

## Slide 20: Scheduling Hierarchically with Conflict Matrices
The Bluespec Compiler compiles modules with (* synthesize *) attributes separately
  The inner-most modules are compiled first
  For each module, the compiler organizes rules into a list scheduler and computes which rules conflict with each other
  The compiler produces a CM for the interface methods which is used when compiling outer modules
Modules that are not compiled separately are effectively inlined wherever they are used
Currently the compiler doesn’t allow separate compilation of a module if it has interface parameters